## DMX controlled laser (channels)
Description	Channel A001	Values
Overall brightness	1	0-255
R, G, B brightness	2, 3, 4	0-255
Strobe	5	0=off, 128=slow, 192=medium, 240=fast, 255=strobe
Turn to angle	6	(channel 7 must be 0) 0=0, 72=90, 137=180, 202=270 degrees AC (approx 1.333 deg per value increment but not linear). Initial angle is set by where chan 7 left it.
Turn continuously	7	0=stop, 1=fast AC, 64=medium AC, 127=slow AC, 128=slow CW, 192=med CW, 255=fast CW. When channel 7 returns to 0 the mirrors will turn AC by the amount set in channel 6 before stopping.
Automatics	8	101, 125, 150=slow, med, fast random, flashing, 151, 175, 200=slow, med, fast random, fading, 201, 225, 250=slow, med, fast random, fading (sparser than 151-200), 251-255=sound activated

## DMX controlled RGB flood lights

Description	Channel	Values
Overall brightness	1	0-255 (channel 6 must be 0-10)
R, G, B brightness	2, 3, 4	0-255 (channel 6 must be 0-10)
Strobe	5	0=off, 128=slow, 192=medium, 240=fast (channel 6 must be 0-10)
Colour change	6	0-10 no effect, 11-60=static (hue controlled by channel 7), / 61-110=smooth transition, 111-160=smooth transition through black, / 161-210=colour sequence, / (for 61-210 speed is controlled by channel 7) / 211-255=sound activated sequence
Hue or / Transition speed	7	(channel 6 must be 11-60) 0=red, via 43=yellow to 85=green, via 128=cyan to 170=blue, via 213=magenta to 255=nearly red / (channel 6 must be 11-210) 0=stop, 32=5s, 128=3s, 192=2s, 255=1s
Automatics	8	101, 125, 150=slow, med, fast random, flashing, 151, 175, 200=slow, med, fast random, fading, 201, 225, 250=slow, med, fast random, fading (sparser than 151-200), 251-255=sound activated

	0-42	43-85	86-128	129-171	172-215	216-258
Red	100	100-0	0	0	0-100	100
Green	0-100	100	100	100-0	0	0
Blue	0	0	0-100	100	100	100-0

R=min(510-6*v, 255)