## DMX controlled laser (channels)
Description	Channel A001	Values
Overall brightness	1	0-255
R, G, B brightness	2, 3, 4	0-255
Strobe	5	0=off, 128=slow, 192=medium, 240=fast, 255=strobe
Turn to angle	6	(channel 7 must be 0) 0=0, 72=90, 137=180, 202=270 degrees AC (approx 1.333 deg per value increment but not linear). Initial angle is set by where chan 7 left it.
Turn continuously	7	0=stop, 1=fast AC, 64=medium AC, 127=slow AC, 128=slow CW, 192=med CW, 255=fast CW. When channel 7 returns to 0 the mirrors will turn AC by the amount set in channel 6 before stopping.
Automatics	8	101, 125, 150=slow, med, fast random, flashing, 151, 175, 200=slow, med, fast random, fading, 201, 225, 250=slow, med, fast random, fading (sparser than 151-200), 251-255=sound activated

## UK36: DMX controlled RGB flood lights (U.King 36 LED 8 Channel)

Description	Channel	Values
Overall brightness	1	0-255 (channel 6 must be 0-10)
R, G, B brightness	2, 3, 4	0-255 (channel 6 must be 0-10)
Strobe	5	0=off, 128=v.slow(2.5s), 192=slow(1/s), 224=med(2/s), 240=fast (channel 6 must be 0-10)
Colour change	6	0-10 no effect, 11-60=static (hue controlled by channel 7), / 61-110=smooth transition, 111-160=smooth transition through black, / 161-210=colour sequence, / (for 61-210 speed is controlled by channel 7) / 211-255=sound activated sequence
Hue or / Transition speed	7	(channel 6 must be 11-60) 0=red, via 43=yellow to 85=green, via 128=cyan to 170=blue, via 213=magenta to 255=nearly red / (channel 6 must be 11-210) 0=stop, 32=5s, 128=3s, 192=2s, 255=1s
Automatics	8	101, 125, 150=slow, med, fast random, flashing, 151, 175, 200=slow, med, fast random, fading, 201, 225, 250=slow, med, fast random, fading (sparser than 151-200), 251-255=sound activated

	0-42	43-85	86-128	129-171	172-215	216-258
Red	100	100-0	0	0	0-100	100
Green	0-100	100	100	100-0	0	0
Blue	0	0	0-100	100	100	100-0

R=min(510-6*v, 255)
## WP6: DMX controlled waterproof RGBW flood lights (6 LED 8 Channel)

Description	Channel	Values
Overall brightness	1	0-255 (channel 7 must be 0-50)
R, G, B, W brightness	2, 3, 4, 5	0-255 (channel 7 must be 0-50)
Strobe	6	0=off, 5=slow(1/s), 128=medium(2/s), 220=fast, 240=flicker (channel 7 must be 0-50)
Colour change	7	0-50 no effect, 51-100=static (hue controlled by channel 8), / 101-150=square transition, 151-200=sine transition, 201-250=triangle transition (for 101-250 speed is controlled by channel 8) / 251-255=sound activated sequence
Hue / Square speed / Sine speed / Triangle speed	8	(channel 7 must be 50-100) 0-31=red, 32-63=green, 64-95=blue, 96-127=grey, 128-159=yellow, 160-191=magenta, 192-223=cyan, 224-255=white / (channel 7 must be 101-150) 0=stop, 128=6s/colour, 180=4s/colour, 220=2s/colour, 240=8s/cycle, 250=2s/cycle, 255=1s/cycle / (channel 7 must be 151-200) 0=stop, 200=3mins/cycle, 255=40s/cycle / (channel 7 must be 201-250) 0=stop, 200=1min/cycle, 255=15s/cycle

## SS54: DMX controlled RGB flood lights (54 LED 7 Channel)

Description	Channel	Values
Overall brightness	1	0-255 (channel 6 must be 0-50)
R, G, B brightness	2, 3, 4	0-255 (channel 6 must be 0-50)
Strobe	5	0=off, 240=v.slow(2s), 250=slow(1/s), 254=medium(2/s), 255=fast (channel 6 must be 0-50)
Colour change	6	0-50 no effect, 51-100=static (hue controlled by channel 7), / 101-150=square transition, 151-200=sine transition, 201-250=triangle transition (for 101-250 speed is controlled by channel 8) / 251-255=sound activated sequence
Hue / Square speed / Sine speed / Triangle speed	7	(channel 6 must be 50-100) 0-31=red, 32-63=green, 64-95=blue, 96-127=grey, 128-159=yellow, 160-191=magenta, 192-223=cyan, 224-255=white / (channel 6 must be 101-150) 0=stop, 128=5s/colour, 180=2.5s/colour, 220=2s/colour, 240=12s/cycle, 250=10s/cycle, 255=8s/cycle / (channel 6 must be 151-200) 0=stop, 240=3.5mins/cycle, 255=50s/cycle / (channel 6 must be 201-250) 0=stop, 254=40s/cycle, 255=20s/cycle